ASC365 8IN1 Heat Press Instruction

ASC365 INTERNATIONAL LTD

sales@asc365.com

www.asc365.com

Description:
8IN1 Heat Press can imprint T-shirts, Ceramic Plates, Ceramic Tiles, Mugs, Mouse Pads, Jigsaw Puzzles, Fabrics & Materials, and Other Misc.

Specification:
Package Weight: 35kg
Size (L W,H): 21.65"x19.29"x19.69" (55cmx49cmx50cm)
Voltage: 110V (If need 220V,contact us)
Temperature: 0~400 degrees C
Time Range: 0~999 Seconds
Heater size: Diameter φ7.5~9cm or φ5~7.5 for Mug
Diameter 12.5cm and 15.5cm for Plate
Diameter 30X38cm for Flat
Diameter 14X8.5cm for cap
Cone-shape mug heater for 12oz and 17oz latte mugs

Instruction For The Digital Showing Panel

1. Push the left “SET” key, you can press up and down key to adjust the heating temp.

2. Push the right “SET” key, you can press up and down key to adjust the heating time.

Change Component for Different Purpose:

1. Fabrication Diagram of Flat Heat Press

2. Fabrication Diagram of Cap Press

Take off the ring pressure gauge and the bottom plate, then put on the top heating plate and cap heating plate, put on the bottom plate and the ring pressure guage and fasten them.

3. Fabrication Diagram of Flat Heat Press

Take off the top and the bottom plate of cap part, change on the flat bottom plate, then fix on the plate heating part and begin the plate printing.( according to the related plate size and suitable fixer size.)

4. Fabrication Diagram of Mug Press