Instruction of ASC6060 Screen Stretcher

This equipment is used for stretching silk screen during making screen plate. It is small in size without taking space. Besides, it can stretch the silk screen evenly, so it is the most important ancillary equipment for making screen plate.

Main Features

- Consisted by four 24"(60cm) wide collets. One single set can apply to any screen frames below 24"x24"(60x60cm) (external dimension), two sets combination can be done all size screen frames below 48"x48" (120x120cm)

- Wide locking bars for compressing screen are critical parts, directly influencing the quality of stretching. We specially exploit concave and convex locking bars made of rubber with proper rigidity, 24" width and no joints

- Suits for any frames below 2” (5cm) thickness (common thickness is 1" - 1.2" / 2.5cm – 3cm). Adjusting position bolt can meet your different requirements.

- Considering machine structure, only some components needs to endure force, we bring in 0.12" (0.3cm) thickness steel plate to make normal components and 0.2" (0.5cm) thickness plate to make forced parts.

Installations

Install gibs                  Install handles of hand wheel

Applications

Make Screens             Make Screens              Make Screens

of 24”x24” (60x60cm)   below 24”x24”(60x60cm)  above 24”x24”(60x60cm)

Parameters

- Crate dimension: 28"*19"*11"(70×48×28cm)

- Net weight: 42Lb(19kg)

- Shipping weight: 50Lb(23kg)

ASC365 International Ltd

http://asc365.com