Instruction of 1800W Flash Dryer

Installations

For convenient transportation, parts of the machine have been uninstalled. Please install them in reference to the video before using.

Operations

1. After well installed, connect the power supply.

2. Turn on the switch and then it will work automatically.

3. Put the probe of the thermometer on the drying table, heat for some time (20 minutes in reference), and then check the actual temp. If the temp is too low or too high, just risen or lower the height of the drying box.

Reference Data

Based on our test, in the condition of 75℉ (24℃) room temperature and no air flowing around the dryer, when the flash dryer has been working for about 30 minutes, the maximum temp of 0.79” (2cm)) below the Drying Box can reach about 374℉ (190℃).

Tips

The temp has keen relations with the distance from the drying box and continuous working time, in addition to the environmental factors (e.g. air flow, room temp, etc.).

Temp Test Instructions

Parameters

Input voltage: 110V

Input power: 1800W

Baking area: 18”x24” (45x60cm)

Maximum temperature: 374℉ (190℃)

ASC365 International Ltd

http://asc365.com