Pad Printing Manual

1)Put the machine on flat ground and turn on the power.

2)Press adjusting switch， the rubber pad moving over the working table.Loosen the adjusting screw, take out the cartridge, wipping oil of pad pringting plate and cartridge by cloth moistened diluent. (In order not to damage the sealing of the cartridge,couldn't scratch with a hard object.Placing the cartridge, the knife edge is up)

3)Press inching switch,rubber pad moving over plate.With a multi-purpose wrench to loosen the nut,so the plate loose.Turn the plate to find the necessary code,moving below the rubber pad,aiming at pad,then use wrench to tightening the nut.

4)Press inching switch,rubber pad moving over working table.Installing the cartridge with oil cup clamp(pressing screw is aimed at three holes on the oil cup ring). Turn on the switch,adjusting the speed to the slowest,screwing pressing screw of three oil cup in turn until the plate can be cleaned.Then screw the nut of the pressing srew.(Don't screw one screw then do others)

5)Pouring prepared ink (ink plus diluent until to automatically flow state) into the cartridge,two-thirds of cartridge volume is best,then covered with ink cover.

6)Adjusting support of pad to contact with plate.

7)Press adjusting switch ,rubber pad moving over the plate.Adjusting the pad seat to make the rubber pad over the code,then tighten the screw.

8)Press adjusting switch.Turn the rotary arm to make the rubber pad turn to the lowest point of working table.Then put the object on the table,the table moves up and down to make rubber pad pressed against the object.(The pressure shouln't be hard,or the code will be out of shape.