2in1 Pulse Sparkle Spot Welder

Description:
1.This item is 2in1 welding machine (1 x Pedestal,1 x Handheld welding gun)
2.Jewelry welding machine can be used for fast welding of platinum, gold , K  gold , silver, steel and precision welding of wires like ends of circle , oval  buckle, fine wire. Argon can be accessed directly without soldering solder  powder , solder joints are smooth and not black .

Installation and trial run:
1.Connect electrode holder to the output cathode; connect anode electrode holder  to the output.
2.Argon via the argon gas valve is connected to its output argon 
3.Tungsten needle can be sharpened in grinding machine, that is to use  sophisticated power management working principals . Inlet valve adjusted to  argon ( argon models are applicable ) 
4.When installing tungsten needle, please make it protrude the welding head  about 5MM . tungsten needle diameter is about 1mm.

Operation:
1.Turn on the power switch.
2. Adjust the power knob. The general adjustment scale ( according to diameter  of the part ) is 1 to 1.5 , ( fine ) adjustment scale is 7-8 (Can be adjusted  according to scale of work requirements)
3. Hold the parts with tweezers and focus the end of the part to the tungsten  needle (optimal distance is 5mm) ,the whole part can not touch the tungsten  needle.
4. Stamp the foot switch. (then stepping away immediately). Welding is  completed.

Parameter:
1. Voltage:110V(if you need 220V, please contact with us)
2. Power:200W
3. Maximum current:30A
4. Weight:5KG/Set