10 Head Ultrasonic Mister

High mist production  capacity, minimum 3000mL/hr.
Durable ultrasonic humidifying module with energy saving.
Minimum water level shut down protection.
60C over temperature shut down protection.
Input voltage polarity protection. (No operation as incorrect polarity)
Power delay ON protection to prevent voltage surge.
Each mist making head with individual circuit and will not completely  shut down as one of heads failure.
Each mist making head with auto-tuned current limiter to prevent over  current drain.
Note :This item is only a part, couldn't use the mister without DC Power

Specifications

| Dimensions | 252L*90W*55mmH(9.9”*3.5”*2.2”) |
| --- | --- |
| Input Voltage(Mist Generator) | DC48V |
| Working current | 4.8~5A |
| Power Consumption | 300W maximum |
| Output Mist Capacity | 3000~4500ml/hr |
| Cooling way | Air cooling |
| Weight | 1.8Kg |