SCREEN REPAIR LCD SEPARATOR USER MANUAL

------------------------------------------------------------------------------------------------------------------------------------------------------------------------

Screen Repair LCD Separator 
Instructions

---------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

Los Angeles,USA Office Address:426 SOUTH PALM AVENUE  ALHAMBRA，CA 91803  United States  Tel:626-415-6138 Email: hugo@asc365.com

Vancouver,CANADA Office Goldbar Plaza,20800 Westminster Hwy. Unit# 2128, Richmond, BC, V6V 2W3   Canada Tel:778-321-6419 Email:salespacific@asc365.com

Toronto,CANADA Office 2220 Midland Ave. Unit 39-41AP  Scarborough, ON, M1P 3E6  Canada Tel:647-350-2889, 416-727-3877, 416-640-1809  Email: sales@asc365.com

1. Product Instruction

Use this wonderful machine if you want to separate the LCD from the touch screen on devices, when the LCD is still functioning as it should. No need to purchase the whole assembly anymore if a screen is cracked!!
▲ Auto heating metal plate, maximum temperature is 400 centigrade.
▲ Safety power system inside, avoiding the problem of electric leakage.
▲ Anti static body material, prevent the LCD and the flex cable being damaged from the static. 
▲ Easy installation. 4 stronger arms to press the touch screen glass on the plate. Smooth metal plate to hold the touch screen without any damaged 
▲ Power supply: AC 85V to AC 265V 50Hz , almost for users from all over the world. Temperature should be set to 80 centigrade to 100 centigrade, when you do the job on iphone and galaxy series etc. 
▲ 2 bearings to last long the life of the wire you use to separate, and prevent your hands be hurt by the high temperature platform 
▲ Compatible for LCD or LED screen assembly

2. Features
This is screen separator machine, it can put glass separated from the LCD screen For iphone 4 4S 5 Samsung S3 S4 NOTE and so on.

1) New Model, more precision - railing to support use of wire
2) Heating plate is made of integrative alloy-aluminum with distributed heat conduction, and will stay in shape though under high temperature
3) With 4 adjustable fixed tools to hold your replacement parts on the machine firmly
4) Comes with refurbishment mould, 50m alloy wire, UV LOCA adhesive glue, UV germicidal lamp, all this accessories can make the operation easily
5) The separate machine is suitable for cell phones of 10 ~ 17cm in length

3. Parameters 
Item Name: Screen Repair machine Kit
Compatible Model: all iPhone 4 4s 5, Samsung S3 S4 NOTE, etc.
Condition: New in box

Colors: Yellow bakelite shell

Gross Weight: 10 KG（22 lbs）

Voltage: 110v (Please contact us for 220V machine)

4. Operation Guidance (Details Video guidance can be found in our Ebay item’s instruction ,or you can email us for the link)

1) – Put LCD panel on the machine plate
2) - Fix panel by 4 clamping tools
3) - Power the machine to produce 100 degrees
4) -Use strong alloy wire to separate the LCD and glass
5) - Use molding that was selected and glue provided for replacing the screen

Note: Please do not set the temperature to more than 120 degrees, because it may damage the screen

5. Packing List

| Screen Separator With Power Cable * Voltage: 110v (Please contact us for 220V machine) * The separate machine is suitable for cell phones of 10~17 cm in length. * The latest model, more precision. Railing to support use of wire. * Yellow bakelite shell. * Heating plate is is made of integrative alloy aluminum with distributed heat conduction, will stay in shape though under high temperature. * Four adjustable fixed tools to hold your replacement parts on the machine firmly. | UV Glue Dryer Light 1 pc * Voltage: 110v (Please contact us for 220V ) * Mainly used to dry the glue after gluing LCD to glass, making your LCD stick to glass firmly without glue trace. * Usage: Click the UV light ON and put the phone near the UV light (as the picture shows), then waiting for the glue dried. Note: Because ultraviolet radiation easy to sunburn the skin, so please wear sunglasses, long-sleeved clothing and rubber gloves when using this lamp. |
| --- | --- |
| Glass Boards | 1 pair Roller | Clean Wiper | Glue Remover |
| iphone 4 glass board 1 pc iphone 5 glass board 1 pc GalaxyS2 glass board 1 pc GalaxyS3 glass board 1 pc GalaxyS4 glass board 1 pc | It's for gold wire to separate LCD screen | About 100 pcs per pack, 4” x 4” per piece | Special formula for removing Liquid Optical Clear Adhesive from LCD screen assemblies. |
| Holders | Gold Wire | UV Liquid Optical Clear Adhesive | Manual Instruction |
| Iphone 4/4s Holder 1 pc Iphone 5 Holder 1 pc Galaxy Note 2 N7100 Holder 1 pc Galaxy Nexus I9250 Holder 1 pc Galaxy s4 i9500 Holder 1 pc Galaxy s3 i9300 Holder 1 pc Galaxy Note I9220 Holder 1 pc | Length: 50m (164 ft) Diameter: 0.1mm Material: Gold wire. High hardness, high wear resistance, high toughness, high tensile strength. It’s used in cutting, and refurbishing LCD. | Material: Acrylic Usage: Touch panel screen and LCD screen. Weight: 50 g One piece 50g UV glue can be applied for 30 glasses. |  |

---------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------

Los Angeles,USA Office Address:426 SOUTH PALM AVENUE  ALHAMBRA，CA 91803  United States  Tel:626-415-6138 Email: hugo@asc365.com

Vancouver,CANADA Office Goldbar Plaza,20800 Westminster Hwy. Unit# 2128, Richmond, BC, V6V 2W3   Canada Tel:778-321-6419 Email:salespacific@asc365.com

Toronto,CANADA Office 2220 Midland Ave. Unit 39-41AP  Scarborough, ON, M1P 3E6  Canada Tel:647-350-2889, 416-727-3877, 416-640-1809  Email: sales@asc365.com