| Number | 01 | 02 | 03 | 04 |
| --- | --- | --- | --- | --- |
| Name | Capping Head | Connecting Shaft | Screw | Screw Head Cap Covering |
| Number | 05 | 06 | 07 | 08 |
| Name | Screw Rubber Pad | Nut | Switch | Change-over Switch |
| Number | 09 | 10 | 12 |  |
| Name | Insurance Block | Power Indicator | Plug |  |

SG-1550  Bottle Capping Machine

一、Specification：

1、Voltage：AC220V±10%  50/60Hz

2、Power：80（W）

3、Operation method: Electric Capping

4、Capping diameter：￠10~￠50（mm）

5、Application bottle Height: All

6、Size：7×7×30（cm）

7、Net Weight：1kg

二、Application：

Suits for all kinds of the High strength bottle caps capping working.，it can also be used with stent.

三、Operation Instruction：

1、Firstly, choosing screw rubbers pad(05) in line with cap size （including￠10~￠20、￠20~￠30、￠30~￠40、￠40~￠50）.Secondly, putting it in the screw head cap covering(04).Thirdly,screwing on the capping head（01）.Finally, putting it in the connecting shaft of main machine（02），tightening the screw（03）

2、Plugging in (12),then the power indicator is on(10)

3、Pressing the switch(07),according to the thread direction of caps，adjusting the change-over switch（08）

4、Setting the cap on the bottle，then aiming screw head cap covering with the cap to open the machine ,to tight the cap.If the resistance of cap is too large, the cap will untighted,we need to adjust the nut（06）to change the pressure,until the cap is hard .

四、Packing List

| Number | Name | Unit | Quantity |
| --- | --- | --- | --- |
| 1 | Main Machine | set | 1 |
| 2 | Screw Head Cap Covering | pcs | 2 |
| 3 | Screw Rubber Pad | pcs | 4 |
| 4 | Manual | pc | 1 |
| 5 | Certification | pc | 1 |