Metal sheet Heat Transfer production package

The metal sheet heat transfer technology is one kind of heat transfer technology, and it is the method of applying vividly a gorgeous quality image which is designed in computer and printed on a sublimation paper (photo, pattern, sign, medal etc.) to a variety of sheet metal coated through heat transfer.

Metal Imaging Products are good resistance to fire, water, acids and alkalis, which can be permanent preserved, and their clarity, color saturation, image depth are just like the original photo. The surface of metal sheet is glossy as a mirror with strong metal texture, and more beautiful than the paper imaging products. The metal sheet heat transfer technology overcomes the defects that traditional paper photos are easily damp and faded, yellow by light, single effect, and no long-term preservation etc. Especially suitable for the production of a variety of medals, merchandise sales license, agent license, honor certificates, commemorative Plates, thank-you plates, metal photographs, birth plates, graduation photos, company logos, house numbers, metal licensing plates, metal signs, metal business cards, cosmetic mirror box panels, metal key ring panels, etc.

We fully consider the buyer’s requirements, equipped with all kinds of equipments and materials about sublimation metal sheet cutting and printing technology, including the high quality heat press machine and high-precision sheet metal cutter which are designed professionally and made by our company, professional design and production of plate heat transfer machine and, and equipped with six metal plates coated with heat transfer, and various brackets, you can placed the metal products on the table, cabinets, etc. In addition, we have specialized technical services and the detailed instruction and operation video, buyers do not need to worry about, and buy this combination the business can be started, no additional purchase of other materials, smaller investment, and satisfactory return.

Package List:

1）Sheet metal cutter 1 set

2）Pearly luster white sheet metal 1pc

3）Pearly luster gold sheet metal 1pc

4）Pearly luster silver sheet metal 1pc

5）White sheet metal 1pc

6）Gold sheet metal 1pc

7）silver sheet metal 1pc

8）5cm*22m (2*866”) High temperature resistant double-sided tape 1roll

9）Drill bits (1.5,2,2.5,3,3.2,3.5,4,4.5,4.8,5,5.5,6,6.5mm, total 13pcs) 1set

10）Blu Tack original re-usable adhesive 1box

11）5.7*2" White Scalar Bracket 12pcs

12）4.6*1.85” White Scalar Bracket 12pcs

13）5.3*1.5cm (2.1*0.6”) Hook Pin 12pcs

14）2*0.8” Hook 12pcs

15）1.6*0.8” Hook 12pcs

16）1.2*0.6” Hook 12pcs

17）ASC1515PB-A110 Heat press machine 1set

18）USA Sublimation Ink（CMYK each color100ml）1set

19）110VHair Drier 1set

20）Card Reader 1pc

21）A4 Sublimation Paper 100pcs

22）20W Mini Glue Gun（110-220V used） 1set

23）Hot Melt Glue（length18cm, thick7mm） 24pcs

ASC1515PB-A110 Heat Press Machine

1. Advantages:

1) Celsius temperature and Fahrenheit degree are changed alternatively, which can be used for countries and areas using different temperature schedules.

2) Intelligent heating function (this unique technique is owned by us): for the power of heating plates of 15*15 inch and above are normally between 1700-2500W, and the current is between 16A-22A. Normally, the damage on the circuit caused by over power consumption in short time, such as trip, fuse blown and over-hot power line will happen for the power line in temporary and public area, lack of current or power is not enough. It is specially designed for this problem and solves it efficiently. This is the important advantage different from others.

3) The multifunction meter along with high quality solid state relay, special louver board and fun to guarantee the machine works for long time. This meter solves the shortages such as the sound of state relay is noisy and the life time of touch spot is short.

4) Intellectualization is high, function is more completed and the operation is easier. What you do is only to adjust 4 keys to set every function and all the setting parameters will be remembered automatically and will not be changed because of de-energizing and stoppage.

5) The control of temp is exacter. The normal meter can’t control the inertial rapid-height of heating plate. For this problem, this meter adopts intelligent temp control technique that measure temp correctly and control temp of heating plate all the time to control temp more correctly.

6) It is easier to maintain and the shipping charge is lower. Our products are adopted combined and separable structure. If the electronic part is broken and needed maintenance, instead sending us the whole machine, you only need to detach it from the machine and send it to us. And then connect the circuit following the wiring diagram to make machine work.

2. Parameters:

Heat-press effective size: 38cm*38cm（15*15inch）

Input voltage: 110V/220V

Heating plate power: 1700w

The highest temperature: 210C (410F)

Heat- press time: 0-999s

Machine size (cm): length 62, width 40, height 37

Outer Packing size (cm): length 71, width 48, height: 45

Weight: 31.5kg

3. Operational Methods:

1，Adjust pressure 1）Adjust the pressure of heat-press plate. Try the pressure first--put printing stock on the base board, press the handle. It will affect the quality of finished product if it's too tight or too loose. Adjust the pressure by the button until suitable. 2) Lift the upper plate and get printing stock out. 3) Turn on power.

2，Set the temp indication, temp, heating time and heating way 1）Set temp indication：℉ or ℃ Press “SET ” key, “Mode” indicates “1”; and “D4” indicates “℃”, which shows the temp of this machine is ℃ Press “+” key once, “Mode” still indicates “1”; and “D4” indicates “℉”, which shows the temp of this machine is ℉ Press “+” and “-” keys alternatively, “Mode” still indicates “1”; and “D4” indicates “℉” and “℃” alternatively. Tip：Please be aware that different districts use different standard. Below is unit conversion chart between centigrade and Fahrenheit. F=1.8C+32 220C=428F 200C=392F 190C=374F 180C=356F 160C=320F 140C=284F

2）Set the highest working time： Press “SET” key, “Mode” indicates “2”, “D1, D2, D3” indicates the assessed temp and “D4” indicates the assessed number at the first step. Press “+” key To increase the temp and press “-” key to reduce it. “D4” indicates “℉”, which means that the temp of this machine is ℉ and the max. assessed temp is 392F ; “D4” indicates “℃”, which means that the tem of this machine is “℃” and the max. assessed temp is 200℃ Tip: Set the suitable temp according to the different T-shirt transfer paper. The highest heating temp of ASC black T-shirt transfer paper is 165℃ or 329℉. The highest heating temp of ASC light T-shirt transfer paper is 185℃ or 365℉.

3）Set the heating time：（This is the keeping time after the machine reaches the assessed time） Press “SET” key，“Mode” indicates “3”; “D1, D2, D3” indicates the assessed heating time and “D4” indicates “s” Press “+” key to increase the heating time and press “-” to reduce it. Tip: Set the suitable heating time according to the different T-shirt transfer paper. The highest heating time of ASC black T-shirt transfer paper is 25s. The highest heating time of ASC light T-shirt transfer paper is 25s

4）Heating way set：（（Hint: when the “MODE” is set “4”，only set “D3” as “0”，other are not the setting functions of this machine and they can’t be supported.）） “Mode” indicates“4”；press“+”key， “D1，D2，D4” is blank screen；“D3”indicates“0”。

5）Fast heating and slow heating set:（This function is specially developed by our company：It is mainly used for the heating system with high power heating plate. And it can solve the damage on the circuit caused by over power consumption in short time, such as trip, fuse blown and over-hot power line. When MODE indicates 5，press“SET”key，“Mode”indicates“5”； “D1，D2 ，D4”is blank screen； “D3” indicates“0”, the power is on continuously; “D3” indicates “1”: Electrify 9 seconds and cut off 1 second “D3” indicates “2”: Electrify8 seconds and cut off 2 seconds “D3” indicates “3”: Electrify7 seconds and cut off 3 seconds “D3” indicates “4”: Electrify 6 seconds and cut off 4 seconds “D3” indicates “5”: Electrify 5 seconds and cut off 5 seconds “D3” indicates “6”: Electrify 4 seconds and cut off 6 seconds “D3” indicates “7”: Electrify 3 seconds and cut off 7 seconds “D3” indicates “8”: Electrify 2 seconds and cut off 8 seconds “D3” indicates “9”: Electrify 1 seconds and cut off 9 seconds For the heating plate under1700W ， “D3” can be set into“0” For the heating plate between 1700W and 2000W，“D3”can be set into “1”or“2” For the heating plate above 2000W，to guarantee the safety，“D3”can be set into“3”or“4” The power of our 15*15 flat press is 1700w, it is suggested to be set D3 into 0 The power of our 16*24 flat press is 2200w, it is suggested to be set D3 into 3 or 4 （Reference：set D3 into 4，it takes about 35-40mins to heat from indoor temp to 200℃ set D3 into 5，it takes about 50-60mins to heat from indoor temp to 200℃ set D3 into 6，it takes about 80-90mins to heat from indoor temp to 200℃ set D3 into 7,8,or,9，the highest temp can only reach 165℃ instead 200℃

3，After finishing above operations, press SET key continuously, and please check the following set: MODE D1 D2 D3 D4 1 -- -- -- F（or C） 2 3 2 9 F 1 6 5 C 3 -- 2 0 S 4 -- -- 0 -- 5 -- -- 1 --

4，After checking and confirming no error, press “RUN” key, and the machine enters into the assessed working process. 1）In the process of preheating, don’t put the handle down unless the temperature has reached the setting degree. 2）MODE indicates“O”，which means the power is on. 3）The heating plate begins to heat from indoor temp, the meter indicates temp; and the temp is rising. 4）When the temp of heating plate reaches the assessed temp（165℃ or 392℉）, MODE indicates alternative indication of “F” and “O” , which means the power is on and off alternatively at assessed highest temp. 5）Place the printing stock on the board and the transfer paper on a proper place. Then put Teflon paper on the top. 6）Press the handle down and the timer will start to count. 7）Upon hearing buzzer ringing, open the machine and take out the printing stock.

5，Get printing stock out and a complete image will be on the printing stock.

Tips： 1）There’re two ways to remove base paper—“Hot-split” and “cool-peel”. Master the right time and temperature due to different materials. 2）On rare occasions, when the temp close to the highest assessed temp, during the MODE indicates power on “O” and off “F” alternatively, when it is “F”, the temp will be 4-6℃ higher than that when it is “O”. This is because that the power of heating plate is larger, and the voltage is reduced, which is normal. The temp of heating plate under “F” situation is standard. 3）On rare occasions, especially the indoor temp is lower, when the assessed temp is over 190℃ or 374℉, because the heating plate radiate heat faster, the temp can’t reach the assessed temp. If this, you can set the highest temp 4-6℃ or 40-43℉ higher, thus the temp of heating plate will reach 190℃ or 374℉

Metal sheet nibbler cutter

Metal cutting is an aspect of industrial processes, and there are many large-scale facilities which can cut metal plate very simply at present. Some large facilities can be used to cut, such as electric or pneumatic cutting machine, large-scale laser cutting machine, water jet cutting machine, wire cutting etc. Some small cutting tools can also be used to cut, such as manual metal cutter, but after cutting it is difficult to avoid the bend of edges and the inaccuracy of size, in addition, manual metal cutter have certain restriction on the blade length, so cutting a longer metal plate would also be subjected to certain restrictions. This sheet metal nibbler cutter which is designed by our company uses the latest sheet metal cutter and a high precision cutting platform with a slider bar and a ruler, and with this sheet metal cutting machine, the accuracy, safety, and operation of simplicity of sheet metal cutting have been great improved, so sheet metal cutting has become very handy.

The sheet metal cutting table is ideal in all sectors of the iron, copper, aluminum, stainless steel sheet metal cutting to precision line, curve, arc, or other irregular lines and shapes. The device can be widely used in auto repair, small-scale machining, sheet metal production, new product development, and decoration, model processing, teaching experiment, hand-made and so on, especially for cutting sublimation sheet metals to the exact line (aluminum and iron materials) in industry production of heat transfer.

1. Advantages:

1）Operation more safely, and cutting platform, drill and cutter are completely separate, operators only need to move the metal plate to cut;

2）Straight line cutting is more accurately, the cutting table is a PVC table with a standard size, and with a sliding flexible mobile baffle specifying cut size. After you are familiar with the cutter, when cutting sheet metal as straight line on this platform, the errors will be in 0.2-0.5 mm range, which is the cutting precision very highly of its kind.

3）Operation is more neatly. It can not only fix the electric drill and cutter to the cutting platform, and cut the sheet metal by your hands moving it, but also can grasp the drill and cutter with your hands, and cut the sheet metal after fixing it by a vise or other tools.

4）Cutting perfect circle is more accurately. Just need to drill holes in the cutting table according to the circle size to be cut (does not affect the normal use of the cutting table), and drill a hole in the center of the metal to be cut, then use the screws and nuts to fix the sheet metal to the table, and make sure the sheet metal rotate freely around the hole, and the precision of the cutting circle is very high.

2. Technology parameters:

1) Total size of the cutter table: 600* 450*155 mm (23.6*17.7*6.1”)

2) Using the slide rail and the mobile baffle can be fixed to ensure the stability after the baffle fixed.

3) One cutter bar with two cutting head, it can be used by changing direction.

4) The cutting head can be rotated 360 degrees, and it is located before it goes out,

5) Power of electric drill: 350W (220v)

6) Minimum cutting radius: 12mm (0.5”)

7) Maximum cutting thickness: iron: 1.8mm (0.07”), stainless steel plate: 1.2 mm (0.05”) copper and aluminum plate: 2mm (0.08”)

8) Net weight: 11.3kg (25Lbs)

3. Basic configuration

1) Cutting table: one (including the base)

2) Double-headed cutter: one (including one cutting tool)

3) 350W (220V) electric drill: one

4) Cutting tool (alternate): one

5) Installation and maintenance tool kit: one set (includes: screwdriver, wrench, stainless steel oiler, crankshaft, cleaning cloth, etc.)

6) Installing and using video discs

4. Operation methods, replacement of components and maintenance: (Reference: cutting table installed with the use of video)

1）Firstly install the electric drill to the connection of the cutting head;

2）(To cut metal lines for example) Move the slider bar and baffle to the size which the sheet metal need to cut, and tighten the positioning screws;

3）Turn on the electric drill, and press the locking button, then start cutting (the speed can be adjusted as needed)

4）When finished cutting, press the drill switch to exit.

5）During cutting, the hole of rod holder and the material to be cut are vertical, avoiding the cutting head to being broken.(It has been adjusted suitably when it goes out)

6）Rod replacement: Refer to the instruction, open cover, remove the anti-loose nuts, loosen the set screws, and pull out the cutter bar, then re-loaded a cutter bar, and tighten the screws.

7）Rod holder replacement: According to the instruction, rotate the nuts anti-clockwise contracts, and replace the new rod holder.

8）The cutting head should be lubricated by motor oil frequently, especially for cutting aluminum sheet. The cutter has been configured an oilier and motor oil.

9）Slide bearing should be well-preserved and lubricated timely to ensure the smooth slide movement.

Sublimation sheet metal

Sublimation pearly luster white, gold, and silver sheet metals are made of steel material, whose surfaces are covered evenly with a layer of pearl film, and with bright and shiny colors. Sublimation white, gold, silver sheet metals are made of aluminum materials. These sheet metals are suitable for making individual permanent images, which can make metal authorization plates, metal cards, mirror box panels, metal keychain panels, metal photos, all kinds of signs, medals commodity marketing cards, proxy business cards, certificates, plaques, thank cards, wedding photos, baby birth cards, graduation photos, company logos, numbers and so on, high quality, vivid color, and strong adsorption.

Size: 600*300 *0.07 mm (23.6*11.8*0.003”)

Net weight: 0.75 kg/pc (1.65 Lbs)

20W Mini-electronic Glue Gun (110-220V)

Mini-electronic glue gun is the perfect alternative to messy glue bottles and tubes around the home. It is small enough to keep in a kitchen or den drawer and versatile enough to handle all your general home gluing needs, such as crafts or small repairs and mending.

Features:

1) It is an ideal tool for home use, compact and utility. It is used to stick DIY toys, fabrics, wood, paper, glass, ceramics and other items, of the paste and repair furniture and bathroom facilities. Insert a diameter of 7.0-7.5 mm glue stick into the glue gun from behind, and plug in to preheat 5-8 minutes, then pull the trigger to press the melt glue.

2) Adopt a high-tech ceramic PTC thermistor as heating elements, heating speed, temperature accurately, can be used in between 100V to 220V DC or AC power, built-in safety fuse.

Notes:

1) During working, the temperature of the melt glue gun nozzle and the melting glue is high, and the body should not touch them.

2) Because it is with PTC heating element, if it is not used within 15 minutes, please cut off the power, so as not to cause melting down the left glue, and damage to glue gun.

3) When not in use, this tool should be placed in its bracket.

4) Don’t pull the left glue stick out from the glue gun when a glue stick has not be used up, you can plug in and reheat 5-8 minutes to use directly next time.

Usage:

1) Before use, install the bracket included with the gun to the glue gun, and stand up it;

2) Make sure the surface pasted is clean, no oil, no water, no dirt;

3) Insert a diameter of 7.0-7.5 mm glue stick into the glue gun from behind till to the front;

4) Plug in the power to heat;

5) After 5 minutes, the glue will melt, and press the trigger on glue gun, the melted glue will overflow from the glue gun;

6) After using, unplug the power on;

7) When the glue gun is completely cool, and then put the glue gun in the toolbox.

Blu Tack Original re-usable adhesive

Main features:

The original re-usable adhesive is used for pasting posters, sealing doors and windows, cleaning the dust and hair on clothes, fixing frame, etc., and it can be reused. In your high-quality life, it will be used definitely such as on the non-porous surface, paint, wallpaper, glass, metal, etc. (Make sure contact surfaces clean, dry and free of grease, dust). This product is non-toxic, but no edible.

Usage:

It will need a certain pressure.

1) Uneven surface: Cut 3-5 cm long Blu Tack, and knead into spherical, then stick it to the surface;

2) Flat surface: Cut 3-5 cm long Blu Tack and stick it to the negative of the object posted;

3) Press the object posted by your fingers

Notes:

1) Press when use, and save by rolling up when not in use.

2) A small amount of residual Blu Tack can be recycled repeatedly by rolling into small groups.

3) Do not use on the easy absorption of screen printing surface or wax paper.

4) Some faint marks will be left on some surface, you can use remover on citrus based to clean.

5) Pay more attention to removing the Blu Tack after the use of a few months.

6) Do not use it to paste heavy objects.