Instruction of ASC 20”x24” Exposure Unit

Installations

For avoiding damage during transportation, the light tubes haven’t been installed, so please install them as following instructions before using.

1. Open the package, place the machine on the table and then remove the glass from machine carefully.

2. Take out the light tubes, sucker and other accessories.

3. Place the light tubes on light clips one by one, and insert the plugs on the two sides. After that, turn on the power to check if the tubes light or not.

4. Place the glass on the machine with sucker (please refer to manual instruction outside the packing box)

Note: There are a pc of light tube, a pc of Electronic ballast and a pc of protective-tube in reserve.

Operations

1. Turn on the power, and the meter is on.

2. Set exposing time:

a. Press “SET” key, the last indicator of meter shows “S” shining.

b. Press “+” or “-” to set time.

c. After well set your time, press “SET” key again, then “S” stops shining.

d. Press “RUN” key, the tubes are all on (if you have well installed the tubes) and the meter begins counting down.

e. Turn off the power and prepare the exposing materials.

3. Place the film and screen plate on it, turn on the power, press the green key, the machine will begin working according to your set parameters. The light tubes will turn off automatically and buzzer rings after exposure.

4. After expositing, turn off the power.

If you want to exposure again, just place the materials on and press green key again. Then buzzer stops, the lights on and it begins counting down. The machine will work as before.

Note: When you use it to exposure next time, it will work according to your last set parameters because of its automatic data memory functions.

Common troubles and solving methods

1. If the meter or light tubes don’t work, please check the electric fuse tube and the power line. Or change them according to the actual conditions.

2. If some light tube doesn’t work, please check whether the two plugs on the two sides of light tubes are installed tightly. If they are tight, please check light tubes and ballasts. Change them according to actual condition.

Parameters

- Voltage: 110V

- Exposing area：20" X 24" (500x600mm)

- Total Power of light tubes: 160W

- Time setting range: 0s-999s

- Machine size: 31”x24.4”x6.7” (790×570×170mm)

- Crate Dimensions: 33"X25"X10"(840×620×250mm）

- Net weight：59.4Lb (27kg)

- Shipping weight: 73Lb (33kg)

ASC365 International Ltd

http://asc365.com