Instruction of ASC-C Flash Dryer

Usages

It is used to dry the screen and drapery screen after printing.

Features

1. Its temp increases quickly for adopting far-infrared modulator tubes.

2. High heating efficiency: Six heating tubes (500W of each) make the temp increase quickly with more even but high heating efficiency system.

3. It adopts hierarchical (100 levels) temp-adjusting system, which makes a more accurate temp control.

Installations & Operations

For convenient transportation, parts of machine have been uninstalled. Please install them in reference to the video before using.

1. After well installed, connect power supply, turn on the switch and then it will work automatically.

2. It adopts hierarchical (100 levels) temp-adjusting system, just click "+" and "-" to set hierarchical level for realizing temp controlling.

Tips

The temp has keen relations with your set hierarchical levels and working time, in addition to environmental factors (e.g. air flow, room temp, etc.). 
We offer a digital thermometer; you can use it to check the actual temp of 1.2” (3cm) below Main Case and adjust the hierarchical level for actual demands.

Reference Parameters

Based on our test, in the condition of 75℉ (24℃) room temp and no air flowing around the dryer, the actual temp of 1.2” (3cm)) below the Main Case are:

(Notes: The temp reference parameters we supplied are six minutes later after hierarchical level adjusted.)

1) If you set “10”,

the actual temp of 1.2” (3cm) below Main Case is 88℉(31℃)

2) If you set “15”,

the actual temp of 1.2” (3cm) below the Main Case is 115℉(46℃)

3) If you set “20,

the actual temp of 1.2” (3cm) below the Main Case is 147℉ (64℃)

4) If you set “25,

the actual temp of 1.2” (3cm) below the Main Case is 180℉ (82℃)

5) If you set “30”,

the actual temp of 1.2” (3cm) below the Main Case is 234℉ (112℃)

6) If you set “35”,

the actual temp of 1.2” (3cm) below the Main Case is 280℉(138℃)

7) If you set “40”,

the actual temp of 1.2” (3cm) below the Main Case is 316℉(158℃)

8) If you set “45”,

the actual temp of 1.2” (3cm) below the Main Case is 347℉ (175℃)

9) If you set “50”,

the actual temp of 1.2” (3cm) below the Main Case is 374℉ (190℃)

10) If you set “55”,

the actual temp of 1.2” (3cm) below the Main Case is 419℉ (215℃)

11) If you set “60”,

the actual temp of 1.2” (3cm) below the Main Case is 473℉ (245℃)

......

(Please refer to the parameters while using.)

Test instructions

Put the probe of the thermometer on the drying table, and then set the temp according to the needed drying temp and the provided reference data. Heated for six minutes, please check whether the temp it shows is the same with the needed drying temp;

1) If the temp it shows is higher than your demand, just click "-" to lower the digital shown on the drying box appropriately;

2) If the temp it shows is lower than your demand, just click "+" to add the digital shown on the drying box appropriately.

Parameters

Input voltage/Power：220V/3000W

Baking area: 18”x24” (45x60cm)

Net Weight：70Lb (32kg)

Temp-adjustable hierarchical range: 1-100

Height adjustable range between flash dryer and ground: 27"-45"（69-114cm）

ASC365 International Ltd

http://asc365.com